Linux Security Module
By Billy Keys

---
2001 Linux Kernel Summit
NSA need to enhance the security in the main stream Linux Kernel.
SELinux
General access-control framework for the kernel
Linux Security Module Project

---
More history
In 2002 developers published a paper on the Linux Security module.
2002 Linux Kernel Summit LSM framework was introduced in the Linux kernel 2.5.29
Now in Linux kernel 2.6 the whole LSM patch was included

---
Goals
Replace the Linux 2.4 capability model
Loadable kernel module to provide different security model
ex) superuser logic, POSIX capability logic, Selinux model

---
LSM Add Ons
Security fields into kernel data structures
Calls (called hooks) in certain points into the kernel
Hooks used to have access-control checks
Adds methods to register and unregister security modules
General security system call for communication between user programs and the LSM for security-aware applications. However current version removed these system calls.

---
Hooks
ie Function calls in certain places in the kernel
Ex struct task_struct and struct linux_binprm
  (look in the kernel code for these struct and hooks).
   may be add a picture
Each hook is a function pointer in a global structure called a security_ops.
( Before the LSM people developing access control security like SELinux would have add kernel patch to include some of these hooks. )

---
Example of a hook vfs_mkdir()
(fs/namei.c)
 int vfs_mkdir(struct inode *dir, struct dentry *dentry, int mode){
        if (!dir->i_op || !dir->i_op->mkdir)
        return -EPERM;
        mode &= (S_IRWXUGO|S_ISVTX);
        //controls if it can make a directory
        error = security_inode_mkdir(dir, dentry, mode);
        if (error)
        return error;
        DQUOT_INIT(dir);
        // used to set the security field for a new directory's inode
        error = dir->i_op->mkdir(dir, dentry, mode);
        ....
 }

---
Types of Hooks
Two types of hooks
     1. Manage security fields
        ex) alloc_security and free_security hooks
      1. Perform access control
       ex) inode_permission hook
        checks the permissions for a file or directory

---
struct security_ops
Data structure which have a list of all the hook
Defined include/linux/security.h
    Detailed docs. of each hook is included in this header file
Example
    (lookup the struct security_ops code )

---
        void* Security Fields
Type void * security
Is inserted into major data structures
   Ex) task_struct, super_block, inode, file, net_device ..

---
LSM methods
register_security () (located in security/security.c)
allows a security module to set the security_ops
unregister_security()
Is used to set to the default security of the dummy module hooks

---
        Methods
Used for stacking LSM
mod_reg_security(..)
mod_unreg_security(..)

---
        Diagram
mkdir is
 called
security_inode_mkdir()
hook is called
normal Unix
permission
checking
security_ops->inode_mkdir(..);
call to inode_mkdir()

---
Mandatory Access Control
Denys users from full control over the access to resources that they create.
Security policy	Set up my administrator or learning algorithm

---
How to write a new LSM module
Define a security_operations data object
Fill in functions
Call register_security() in init part of module
Call unregister_security in exit part of module

---
Capabilities (may not use)
Define a set of privileges in a system
     If a process has a capability it can do that action
 total of 29 capabilities
Defined in include/linux/capability.h
#define CAP_KILL 5
.
.

---
Capabilities
capabilities logic was moved out of the core kernel code and into a security module,

---
Different LSM modules

---
Dummy Security Module
 Dummy Security Module
     initialized the set of hook functions
     Traditional superuser logic
Which is initialized by the kernel with a dummy security module of a set of functions before any security module is installed.

---
SELinux
Goal Minimize affects of a compromised process
Comes with the standard Linux kernel
Mandatory Access Control
Computer controls what a process can do not the owner.
Restricts the privileges of process to a minimum
To prevent harm to the system if the process gets attacked
Needs to be configured to setup the security policy of the system

---
        How SELinux works
Based on a military security level
        Level of clearance
Top secret
can't write to
Unclassified

---
        SELinux
Problems:
Complex to setup
Many times disable
Does not use the pathname for it's access control

---
AppArmor
Developed by Novell
Included in open SUSE OS
Started as a kernel patch move to a LSM
Learning mode
Enforce the applications to only be able to access resources aimed to be accessed by the application.

---
        What AppArmor Prevents
compromised
root process
Without a security policy
With a Apprmor
 profile
Attacker can only do a
limited number of things
Attacker can do anything
which root can do

---
      Linux Access Control Chart

---
Debate of the LSM

---
        Linus's Opinions
Reason for not removing the LSM
1. Developers are starting to use LSM
2. Does not want to say which model is the best to use in the Linux kernel

---
Criticism of the LSM
1) Attackers can install root kits as a LSM
2) Overhead even if there is no LSM installed
3) Most of the hooks are not used in most access control software.
4) too few developer are submitting there modules to the Linux kernel

---
Without the LSM
Developers of access control software need to have access to main kernel.
Kernel Patches for access control
Harder for users to install

---
my opinion
Good
Easy way for kernel developers implement different security models for research.
Hybrid of LSM's
Need for a better model other then the current super user model.
Bad
The need for a dummy module (ie slower kernel)
Many Access Control software still require an kernel patch
Most developers are not submitting there LSM to the main stream kernel

---
Reference
http://en.opensuse.org/AppArmor_Detail
http://www.linuxjournal.com/article/9036
Mail list
linux-security-module@vger.kernel.org